## Slide 1: What numbers to store?
Ideally:
  Continuous amount (nearly, discrete quanta of photons)
  Huge range (surface of sun vs. dark room)
Practically:
  Mainly interested in what we can see
  What differences we can tell
  If we’re making pictures, not for analysis

## Slide 2: How sensitive is the eye?
Amazing range!
  Night vision – when eyes adjusted, camping
  Bright daylight
    Sunlight 10000.
    Twilight 10.
    Starlight 0.001
Catch: at any given time, can’t see this range
  Adaptation – bright light, iris closes, lets in less light, …
At any given time, about 100:1 contrast ratio
  This is a lot more than most displays
  Better displays = more constrast
    Often by blacker blacks

## Slide 3: High Dynamic Range Imagery
Most sensors/displays have less range than eye
  Certainly less range than scenes do
What happens?
  Bright areas – all white (no details)
  Dark (shadow) areas – all black (no details)
What to do?
  Adjust exposure (time, aperature, sensitivity) to get the most important stuff
  Acquire “High Dynamic Range” Imagery
    Special sensors
    Multiple exposures (at different settings) – cool thing to do
  HDR later in the course

## Slide 4: Perception of intensity
Eye senses relative differences
  Equivalent differences 50:100 20:40
  Hard to tell absolute differences directly
    Adaptation to current setting
Can sense 1% differences
At any given time 100:1 contrast ratio
How many levels can you see in an image?
  1.01 ^ 463 = 100.2 (e.g. 463 1% differences = 100:1)
  This is about 8 bits of precision (less than 9)
  But its VERY non linear 1, 1.01, …. , 99.2, 100.2

## Slide 5: Non-linearity of intensity
Non-linear mapping from “amount of light” to perceived brightness
Want uniform mapping of intensities -> perception
  Level 1, 2, 3, …. 255 -> 1, 1.01, 1.02, … 99, 100
Worse: displays are non-linear too
  Voltage -> amount of light is non-linear
  Different displays are different
Want to linearize the system
  Intensity levels map nicely to perceived levels

## Slide 6: Gamma correction
Idea: put a non-linear function between intensity and output
  Done as the last step (usually) – after all computations
Could create arbitrary functions for mapping
  Too cumbersome
Exponential is a good approximate model
  Exponential non-linearity of perception
  Exponential power laws in CRTs

## Slide 7: Modeling a display device
5/2 power law (five-halves)
  Models physics of a CRT
  Real CRTs are close, LCDs designed to be similar
L = M (i+)^
  i = input intensity value
  L = amount of light
   = since zero isn’t really black
  M = maximum intensity
   = specific property of display

## Slide 8: Linearizing the display
Define a function g that corrects for non-linearity
L = M ( g(i) )^ (ignoring )
  G = 1/ 
Where do we get  from?
  Pick it so things look right
Note: 1st order approximation (very simple)
  Only 1 parameter to specify (), many factors

## Slide 9: Gamma correction
Want value 0 = minimum intensity
Want value max (1 or 255) = maximum intensity
--- those 2 are easy to get
Pick one more point
  Midpoint should be 50%
  Easy – show 50% black white + 50% gray
  Adjust gamma until it looks the same
All this happens “behind the scenes”
Everything gets harder when we deal with color

## Slide 10: What to store in the frame buffer?
Frame Buffer = rectangular chunk of memory
Intensity measurements
  Deal with color later, basically store multiple monochrome
Continuous range of intensities
  8-9 bits of precision ideally
    More since can’t get exactly right (10-12 bits)
    More since want more dynamic range (12-14 bits)
    More since want linear space to make math easy (16-32 bits)
Discrete set of choices – QUANTIZATION
  Inks, palettes, color tables, …
  Less storage cost + Color table animation